## Slide 1
ETROC bonding diagram
One row of 16 PCB pads are ground
One row of 13 PCB pads are power supplies
Two rows of 31 PCB pads are signals
Smallest PCB pad size : 5x10 mils
Smallest PCB pad pitch : 10.236 mils (0.26 mm)
Smallest bonding wire length : 0.786 mm
Longest bonding wire length : 1.675 mm

## Slide 2
ETROC2 |  |  |  |  | 
PCB pin# | Pin name | Die pad# | PCB pin# | Pin name | Die pad#
1 | VSS_A | 1-6 | 23 | DORN | 71
2 | VREF | 7 | 24 | VDD_D | 72-78
3 | VDD_A | 8-13 | 25 | VSS_D | 79-82
4 | VSS_A | 14-21 | 26 | ADDR0 | 83
5 | VDD_A | 22-26 | 27 | ADDR1 | 84
6 | VSS_AD | 27-32 | 28 | ADDR2 | 85
7 | VDD_D | 33-40 | 29 | RSTn | 86
8 | VSS_D | 41-47,49 | 30 | VSS_D | 87
9 | VP | 48 | 31 | VDD_D | 88
10 | VDD_D | 50-52 | 32 | SCL | 89
11 | CLK40P | 53 | 33 | SDA | 90
12 | VSS_D | 54,56,58,40 | 34 | ADDR3 | 91
13 | CLK40N | 55 | 35 | ADDR4 | 92
14 | CLK1280P | 57 | 36 | VSS_D | 93-95
15 | CLK1280N | 59 | 37 | VDD_EFUSE | 96
16 | FCP | 61 | 38 | VSS_D | 97-104
17 | VDD_D | 62,64,66 | 39 | VDD_A | 105-109
18 | FCN | 63 | 40 | VSS_D | 110-111
19 | DOLP | 65 | 41 | VDD_A | 112-117
20 | DOLN | 67 | 42 | VSS_D | 118,120-124
21 | VSS_D | 68,70 | 43 | VTEMP | 119
22 | DORP | 69 |  |  | 
Wave Sample |  | 
PCB pin# | Pin name | Die pad#
WS01 | DVSS | WS01
WS02 | DVDD | WS02
WS03 | ADDR4 | WS03
WS04 | ADDR3 | WS04
WS05 | ADDR2 | WS05
WS06 | ADDR1 | WS06
WS07 | ADDR0 | WS07
WS08 | WR_EN | WS08
WS09 | DVSS | WS09
WS10 | DVDD | WS10
WS11 | AVSS | WS11,WS13
WS12 | AVDD | WS12,WS14
WS13 | SCL | WS15
WS14 | SDA | WS16
WS15 | RSTn | WS17
WS16 | AVSS | WS18,WS20
WS17 | AVDD | WS19,WS21
PCB-DIE pin map